DPX Light Response
5.6.2018

---
Daylight - Evening

---
Duty Cycle
- DPX is placed inside a box which is illuminated by an LED
- The LED is pulsed: frequency as well as the duty cycle has influence on the detector’s response!

---
LED Red – 50% duty

---
LED Red – 75% duty
- Periodic structures?
- Also position of LED has large influence on the resulting spectrum

---
LED Blue – 40% duty
- Move light source...
- Change duty cycle…
- Change frequency…
  Until periodic structures manifest!

---
LED Blue – 40% duty
Count the peaks!

---
LED Blue – 40% duty
1
One! One peak!

---
LED Blue – 40% duty
1
2
Two! Two peaks!

---
LED Blue – 40% duty
1
2
3
Three! Three peaks!

---
LED Blue – 40% duty
Where do the peaks come from?
- LED is incoherent and not thermal
- It seems like LED triggers noise in electronics
1
2
3
17
Seventeen!
Seventeen peaks!
Ah ah ah ah...

---
LED Blue - Linearity
- Apply linear fit
- Slight deviation at first and last points
- Slope of 49.1 +/- 0.4

---
LED Blue - FFT

---
LED Blue – Low energies
Not much happening until 2000 ToT...
But...

---
LED Blue – High energies

---
LED Blue – High energies
Let’s count again!

---
LED Blue – High energies
About 38! 38 peaks!

---
LED Blue - Linearity
- Apply linear fit
- Linearity of the pre-amplifier for high energies confirmed?
- Slope of 50.7 +/- 0.2
→ Similar slopes for both ToT-ranges

---
TODO
- Is the phenomenon the same for every pixel?
- Optimize measurement setup
- Per-pixel analysis
- Potential:
  - Proof of linearity of pre-amplifier for high energies
  - ToT-Calibration: scale x-axis until peak positions are the same for each pixel

---
Energy Correction
- Get the peak positions in the spectrum and assign a peak index to them
- Perform linear correction
Uncorrected
Corrected

---
Energy Correction
For high energies
- Different shape after correction
- Seems like fluctuating region gets smaller
Uncorrected
Corrected

---
Reproducibility
Is the result the same for different measurements?
- Performed a large quantity of measurements
- Apply linear correction and store parameters
- Compare maximum deviation, from 0 to 4095 ToT for some measurements

---
TODO
- Measurement with high statistics for each pixel
- Get standard deviation as a function of deposited energy → Useful for simulation
- Evaluate method by performing measurement with radioactive source